SECTION 08360

SECTIONAL OVERHEAD DOORS

PART 1 GENERAL

1.1     SECTION INCLUDES

A.     Sectional  Overhead  Doors

1.2     RELATED SECTIONS

A.     Section 04810-Unit Masonry Assemblies

B.     Section 05100-Structural Metal Framing

C .    Section 06100- Rough Carpentry

D.     Section 09900- Paints and Coatings

E.     Section 16050- Wiring Connections

1.3     REFERENCES

A.     ANSI/DASMA 102-American National Standard Specifications for Sectional Overhead

Type Doors.

1.4     SUBMITTALS

A.     Submit under provisions of Section 01300

B.     Shop Drawings: Show in detail opening and clearance dimensions. Include elevations

of sections and track. Include section finish, gauge and non standard options.

Show detail of jamb material and connections.

C.     Verification Samples: Two samples, minimum 6 inches square, representing actual

actual product selected.

D.     Operation and Maintenance data.

1.5     QUALITY ASSSURANCE

A.     Manufacturer Qualifications: Company specializing in manufacturing products in this

08360-1

section with minimum five years experience.

B.     Installer Qualifications: Authorized representative  of the manufacturer with minimum

five years documented experience.

1.6      DELIVERY, STORAGE AND HANDLING

A.     Store products in manufacturer’s unopened packaging until installation.

B.     Store materials in a dry, weathertight  location.

PART 2 PRODUCTS

2.1     MANUFACTURERS

Acceptable Manufacturers: General Doors Corporation, which is located at One Monroe St.;

Bristol, PA 19007; Tel: 215-788-9277; Fax 215-788-9450; Email:

sales@general-doors.com; Web: www.general-doors.com

2.2     NON-INSULATED STEEL SECTIONAL OVERHEAD DOORS

A.     General Doors Corporation Model 24 Gauge.

1.     Door Assembly: Roll formed steel pan type construction. Doors

comply with:

a.     ANSI/DASMA 102 – American National Standard Specifications for

Sectional Overhead Type Doors.

2.     Door Model: 24 Gauge Non-Insulated

3.     Panel Thickness: 2 inches

4.     Exterior Surface: Roll formed smooth surface with two deep reinforcing ribs

and four shallow grooves.

5.     Exterior Steel: Pre-Painted 0.023 inches, hot dipped galvanized. Two coat

baked on paint system, enamel primer and a 1.0 mil thick polyester finish coat.

6.     End Stiles:

a. Single end caps: 16 gauge galvanized

b. Double end caps: 16 gauge galvanized

7.    Center Stiles: 18 Gauge

8.     Torsion Springs:

a. 10,000 cycles

b. 25,000 cycles

c. 50,000 cycles

d. 75,000 cycles

e. 100,000 cycles

1. Mounted on 1’’ tube (14 ga. Min)

2. Mounted on 1’’ CRS solid shaft keyed full length

9.     Windows:

a. none

b. 24 x 7  1/8” Plexiglass

c. 24 x 7  3/16” Polycarbonate

d. full view aluminum section glazed with 1/8” DSB glass-color matched

e. full view aluminum section glazed with 1/8” tempered glass-color matched

f.  full view aluminum section glazed with 1/8” acrylic(Plexiglass)-color matched

g.  full view aluminum section glazed with 1/8” polycarbonate(Lexan)-color

matched

10.     Exterior Colors:

a. manufacturer’s standard white

b. manufacturer’s standard bronze

08360-2

11.     Wind Load Design:

a. ANSI/DASMA 102 standards to meet applicable code

b. 15 psf/ 90 mph

c. 20 psf/ 105mph

12.     Track and Operating Hardware:

a. Standard lift

b. High lift

c. Vertical Lift

d. Low headroom

e. Roof incline

f. High lift w/ Roof Incline

13.     Hardware: Heavy duty galvanized hinges and fixtures. Floating ball bearing

rollers with hardened steel races. Galvanized aircraft cables, 7x19

construction, minimum 5:1 safety factor.

14.     Lock:

a. Inside slide, spring activated

b. Exterior keyed cylinder with lock bars

15.     Track:

a. 2 inches wide, roll formed galvanized

b. 3 inches wide, roll formed galvanized

16.     Seals:

a. Vinyl weatherseal full width of door, bottom section.

2.3     FABRICATION

A.     Check site dimensions prior to fabrication

PART 3 EXECUTION

3.1     EXAMINATION

A.     Verify opening dimensions, jambs plumb, level and square

3.2     INSTALLATION

A.     Install assembly in accordance with manufacturer’s instructions.

B.     Assemble work plumb, true, square, straight , level and accurate as per drawings

C.     Position jamb weather seal to contact door when closed.

3.4     ADJUSTING

A.     Adjust door to ensure smooth operation through open and close cycle. Use

manufacturer  approved lubricant on all bearings.

3.5     DEMONSTRATION

A.     Demonstrate proper operation to user.

END OF SECTION

08360-3